Drivers of carbon emissions in EU countries before and during the economic crisis

Danae Diakoulaki & Dimitra Kopidou

Laboratory of Industrial & Energy Economics, School of Chemical Engineering, National Technical University of Athens, Zografou

diak@chemeng.ntua.gr, dkopidou@chemeng.ntua.gr

Abstract

The present paper is addressing the challenge faced by European Union (EU) to achieve a sustainable low carbon economy and in particular, to reduce carbon emissions by 20% up to 2020, according to the targets set in its “energy and climate package”. A decomposition analysis is performed in each EU country in order to uncover the explanatory factors behind the changes in CO2 emissions, during the period 2000-2010 and to detect major drivers and common trends. The period under investigation was split into two time intervals, before and during the economic crisis in order to more accurately identify the respective effects of the examined drivers. The decomposition approach used relies on the Log Mean Divisia Index I method. It was found that during the period of economic growth, rising emissions have been offset by significant improvements in energy intensity, denoting a more efficient use of energy resources due to technological and organizational changes. The fuel mix in the economy and in the electricity generation sector seems to play a minor role to emission reduction. The picture is quite different during the economic recession, with energy intensity effect becoming less apparent or even contributing to emissions rise, while changes in the fuel mix appear as the major driver to emission reduction. Finally, structural changes had a limited effect in both periods, although the shift toward the service sector appears to contribute to emission reduction, especially in the most developed EU countries.

Keywords: 	Carbon emissions; decomposition analysis; growth, energy; European Union.

JEL Classification: 	O44; O47; O52; Q43; Q56.

Ερμηνευτικοί παράγοντες της μεταβολής των εκπομπών CO2 στην Ευρωπαϊκή Ένωση πριν και μετά την οικονομική κρίση

Δανάη Διακουλάκη & Δήμητρα Κοπίδου

Εθνικό Μετσόβιο Πολυτεχνείο, Σχολή Χημικών Μηχανικών

Εργαστήριο. Βιομηχανικής & Ενεργειακής Οικονομίας,

Πολυτεχνειούπολη Ζωγράφου Αθήνα 15780

diak@chemeng.ntua.gr,  	dkopidou@chemeng.ntua.gr

Περίληψη

Η Ευρωπαϊκή Ένωση κατέχει σταθερά μία ηγετική θέση στην παγκόσμια προσπάθεια καταπολέμησης της κλιματικής μεταβολής, ενώ στο σύνολο της υπερκάλυψε το στόχο του Κιότο για τη μείωση των εκπομπών αερίων του θερμοκηπίου. Στο επίπεδο των κρατών-μελών όμως, παρατηρείται μία αισθητή διαφοροποίηση των επιδόσεων. Στην εργασία αυτή διερευνώνται οι προσδιοριστικοί παράγοντες που ερμηνεύουν τη μεταβολή των εκπομπών CO2, του πιο σημαντικού αερίου του θερμοκηπίου, κάθε κράτους μέλους της ΕΕ με στόχο να αναδειχθεί ο βαθμός αποσύνδεσης της οικονομικής μεγέθυνσης από το ύψος των εκπομπών, αλλά και η σχετική συμβολή παραμέτρων που σχετίζονται με διαρθρωτικές και τεχνολογικές μεταβολές της οικονομίας τους. Τα αποτελέσματα αναδεικνύουν μία σημαντική αναστροφή της συμβολής των διαφόρων ερμηνευτικών παραμέτρων στην περίοδο μετά την οικονομική κρίση, υποδηλώνοντας μία παράπλευρη αρνητική επίπτωση της ύφεσης στην αποτελεσματικότητα χρήσης των πόρων και κατ’ επέκταση στο περιβάλλον. Η μεθοδολογία που εφαρμόζεται είναι η ανάλυση αποδόμησης (decomposition analysis) και ειδικότερα η μέθοδος  με χρήση δεικτών, Log-Mean Divisia Index I.

Λέξεις Κλειδιά: 	Εκπομπές CO2, Ευρωπαϊκή Ένωση, χρήση δεικτών,

οικονομική κρίση.

JEL Κωδικοί: 	O44, O47, O52, Q43, Q56.

1. Introduction (Εισαγωγή)

Times New Roman, 12

2. Literature Review (Ανασκόπηση Βιβλιογραφίας)

Decomposition methods …. (Hoekstra and Van der Bergh, 2003; Su and Ang,

……………………………………………………………………………………………………………………………………………………………

The present paper is using one of the most widespread IDA methods, the Log ……………………………………………………………………………………………………………………………………………………………………………

3. Methods and Data (Μέθοδοι και Δεδομένα)

For an indicator V defined by means of n factors, x1, x2,…, xn, and assuming that for the period [0-t] its value changes from V0= x10x20…xn0 to Vt= x1tx2t…xnt, this change is decomposed as follows:

(1)

According to the additive LMDI I, the effect of the determinant factor x in Eq. (1) is given by:

(2)

…

3.1 Data (Δεδομένα)

….

3.1.1 The case of Greece (ή Η περίπτωση της Ελλάδας)

……

Table 1: Estimates Basic Multinomial Logit

| Variables | Coefficient | Standard Error |
| --- | --- | --- |

Figure 1: Frequencies of environmental behavior variables

3.2 Methods (Μέθοδοι)

…

4. Empirical Results (ή Εμπειρικά Αποτελέσματα)

…

5. Conclusions (ή Συμπεράσματα)

…

References (Βιβλιογραφία)

Addams H. (2000). Q Methodology. Chapter 2. In: H. Addams and J. Proops. Social Discourse and Environmental Policy: An Application of Q Methodology. Cheltenham: Elgar.

Arrow K, Solow R, Portney P.R, Leamer E.E, Radner R. and Schuman H. (1993). Report of the NOAA Panel on Contingent Valuation, Federal Register 58(10), 4601-4614.

Bateman I. and Turner K. (1992). Evaluation of the Environment: The Contingent Valuation Method, GEC Working Paper 92-18, Centre for Social and Economic Research on the Global Environment (CSERGE), University of East Anglia, Norwich and University College London.

Black J.S, Stern P.C and Elworth J.T. (1985). Personal and contextual influences on household energy adaptations. Journal of Applied Psychology, 70: 3-21.

Bräuer I, Müssner R, Marsden K, Oosterhuis F, Rayment M, Miller C. and Dodoková A. (2006). The use of market incentives to preserve biodiversity. Final report. Ecologic, Berlin, July 2006. Available from:

http://ec.europa.eu/environment/enveco/others/pdf/mbi.pdf

Οι περιγραφές των ενοτήτων (sections) είναι ενδεικτικές και όχι δεσμευτικές.